## Slide 1: POINT-TO-POINT PROTOCOL (PPP)

## Slide 2: Introduction to PPP
It is a communication protocol of the data link layer
It is used to transmit multiprotocol data between two directly connected (point-to-point) computers.
It is a byte - oriented protocol that is widely used in broadband communications having heavy loads and high speeds.
it is a data link layer protocol, data is transmitted in frames.
It is also known as RFC 1661.

## Slide 3: Services Provided by PPP
Defining the frame format of the data to be transmitted.
Defining the procedure of establishing link between two points and exchange of data.
Stating the method of encapsulation of network layer data in the frame.
Stating authentication rules of the communicating devices.
Providing address for network communication.
Providing connections over multiple links.
Supporting a variety of network layer protocols by providing a range of services.
feature of PPP is that it provides network address configuration.

## Slide 4: Services Not Provided by PPP
does not provide flow control
Lack of error control and sequence numbering
does not provide a sophisticated addressing mechanism

## Slide 5: Framing
Flag. A PPP frame starts and ends with a 1-byte flag with the bit pattern 01111110.
Address. The address field in this protocol is a constant value and set to 11111111 (broadcast address).
Control. This field is set to the constant value 00000011
Protocol. defines what is being carried in the data field: either user data or other information.
Payload field . user data : maximum of 1500 bytes
FCS. The frame check sequence (FCS) is simply a 2-byte or 4-byte standard CRC.

## Slide 6: Byte Stuffing
PPP is a byte-oriented protocol, the flag in PPP is a byte that needs to be escaped whenever it appears in the data section of the frame.
The escape byte is 01111101

## Slide 7: Transition Phases

## Slide 8: Multiplexing
PPP is a link-layer protocol
Three sets of protocols are defined to make PPP powerful:
the Link Control Protocol (LCP),
Two Authentication Protocols (APs), and
several Network Control Protocols (NCPs).
Multiplexing is the technology that is able to combine multiple communication signals together in order for them to traverse an otherwise single signal communication medium simultaneously

## Slide 9: Link Control Protocol
is responsible for establishing, maintaining, configuring, and terminating links.
It provides negotiation mechanisms to set options between the two endpoints. Both endpoints of the link must reach an agreement about the options before the link can be established.

## Slide 11: Authentication Protocols
It means validating the identity of a user who needs to access a set of resources.
PPP has created two protocols for authentication:
Password Authentication Protocol and
Challenge Handshake Authentication Protocol.

## Slide 12: Password Authentication Protocol (PAP)
A. The user who wants to access a system sends an authentication identification (usually the user name) and a password.
b. The system checks the validity of the identification and password and either accepts or denies connection.

## Slide 13: Challenge Handshake Authentication Protocol (CHAP)
It is a three-way handshaking authentication protocol that provides greater security than PAP.
In this method, the password is kept secret; it is never sent online.
a. The system sends the user a challenge packet containing a challenge value, usually a few bytes.
b. The user applies a predefined function that takes the challenge value and the user’s own password and creates a result. The user sends the result in the response packet to the system.
c. The system does the same. It applies the same function to the password of the user (known to the system) and the challenge value to create a result. If the

## Slide 16: Network Control Protocols
PPP is a multiple-network-layer protocol.
It can carry a network-layer data packet from protocols defined by the Internet, OSI, Xerox, DECnet, AppleTalk, Novel
For example,
IPCP (Internet Protocol Control Protocol) - configures the link for carrying IP data packets.
Xerox CP does the same for the Xerox protocol data packets

## Slide 17: Network Control Protocols :Internet Protocol Control Protocol (IPCP)

## Slide 18: Multilink PPP
logical PPP frame is divided into several actual PPP frames.
A segment of the logical frame is carried in the payload of an actual PPP frame
In networking, one piece of a data packet that has been broken into smaller pieces in order to accommodate the maximum transmission unit (MTU) size of a network.

## Slide 19
network layer packet as it is transmitted through a
PPP connection. Figure 11.29 shows the steps