## Slide 1: Quality of Service

## Slide 9: Quality of service (QoS)
Quality of service (QoS) refers to a network’s ability to achieve maximum bandwidth and deal with other network performance elements like latency, error rate and uptime.
Quality of service also involves controlling and managing network resources by setting priorities for specific types of data (video, audio, files) on the network.
QoS is exclusively applied to network traffic generated for video on demand, IPTV, VoIP, streaming media, videoconferencing and online gaming.

## Slide 10: Network traffic
It is the amount of data moving across a computer network at any given time.
Network traffic, also called data traffic, is broken down into data packets and sent over a network before being reassembled by the receiving device or computer.

## Slide 11: Quality of service (QoS)
Quality of service (QoS) is the description or measurement of the overall performance of a service, such as a telephony or computer network or a cloud computing service,
particularly the performance seen by the users of the network.
To quantitatively measure quality of service, several related aspects of the network service are often considered, such as packet loss, bit rate, throughput, transmission delay, availability, jitter, etc.

## Slide 12: Quality of service (QoS)
It is the description or measurement of the overall performance of a service, such as a telephony or computer network
It can be referred as efficiency
to provide quality of service for an Internet application
four types of characteristics
reliability, delay, jitter, and bandwidth.

## Slide 13: Reliability
If a packet gets lost or acknowledgement is not received (at sender), the re-transmission of data will be needed. This decreases the reliability.
The importance of the reliability can differ according to the application.
For example: E- mail and file transfer need to have a reliable transmission as compared to that of an audio conferencing.
To delivery of data to intended recipients was successful.
Lack of reliability means losing a packet or acknowledgment
For example, reliable transmission is more important for electronic mail, file transfer, and Internet access than for telephony or audio conferencing.

## Slide 14: Delay
Delay of a message from source to destination is a very important characteristic. However, delay can be tolerated differently by the different applications.
For example: The time delay cannot be tolerated in audio conferencing (needs a minimum time delay), while the time delay in the e-mail or file transfer has less importance.
bit of data to travel across the network from one communication endpoint to another
time it takes to push the packet's bits onto the link
telephony, audio conferencing, video conferencing, and remote logging

## Slide 15: Jitter
Jitter is the variation in delay for packets
For example,
If four packets depart at times 0, 1, 2, 3 and arrive at 20, 21, 22, 23, all have the same delay, 20 units of time.
On the other hand, if the above four packets arrive at 21, 23, 24,and 28, they will have different delays.

## Slide 16: Bandwidth
need to send millions of bits per second
the total number of bits in an e-mail

## Slide 17: FLOW CONTROL TO IMPROVE QOS
A stream of packets from source to destination is called a flow.
Scheduling : FIFO queuing, priority queuing, and weighted fair queuing
Traffic Shaping or Policing: leaky bucket and token bucket.
Resource Reservation : buffer, bandwidth, CPU time
Admission Control : used by a router or a switch to accept or reject a flow based on predefined parameters called flow specifications

## Slide 18: Scheduling : first-in, first-out (FIFO) queuing,
packets wait in a buffer (queue) until the node (router) is ready to process them.
If the average arrival rate is higher than the average processing rate, the queue will fill up and new packets will be discarded.

## Slide 19: Priority Queuing
packets are first assigned to a priority class. Each priority class has its own queue.
The packets in the highest-priority queue are processed first.
Packets in the lowest-priority queue are processed last.

## Slide 20: Weighted Fair Queuing
weighted based on the priority of the queues;
higher priority means a higher weight.
The system processes packets in each queue in a round-robin fashion with the number of packets selected from each queue based on the corresponding weight.

## Slide 21: Traffic Shaping or Policing
To control the amount and the rate of traffic is called traffic shaping or traffic policing
Leaky Bucket : A leaky bucket algorithm shapes bursty traffic into fixed-rate traffic by averaging the data rate. It may drop the packets if the bucket is full.
Flow of the water from bucket is at a constant rate which is independent of water entering the bucket

## Slide 22
The following is an algorithm for variable-length packets:
1. Initialize a counter to n at the tick of the clock.
2. If n is greater than the size of the packet, send the packet and decrement the counter
by the packet size. Repeat this step until the counter value is smaller than the
packet size.
3. Reset the counter to n and go to step 1.

## Slide 23: Token Bucket
The leaky bucket is very restrictive.
It does not credit an idle host.
For example, if a host is not sending for a while, its bucket becomes empty.

## Slide 24
https://www.youtube.com/watch?v=aD_yi5VjF78